Document:		Ignition

Project:	Engine Management System

HMC_V6

Version:	a

Date:	17-Dec-97

Number of pages:	53

Revision Code-No.:	153589 from 18.12.97

Construction protocol-No.:	–––––

Software version:	650H0000

|  | Name | Department | Phone | Date | Sign |
| --- | --- | --- | --- | --- | --- |
| Author | Müller O. | AT PT SI TSA 11 | 3211 | 09.12.97 |
|  | 1. Check | Pioch O. | AT PT SI TSA 11 | 3212 | 09.12.97 |
|  | 2. Check | Gessner S. | AT PT SI TSA 11 | 5398 | 09.12.97 |
|  | Responsible | Brückner D. | AT PT SI TSA 16 | 4279 | 09.12.97 |

Vehicle Electronik Systems Division	Identification No.: 657765.49.05

–––––

Version list

| Version | Date | Author | Comment, Description |
| --- | --- | --- | --- |

Table of contents	Page

1.1 	General

1.1.1 	Total formulas

1.1.1.1 	Ignition angle calculation ( IGA_CYL_(CYL] , IGA_SAM )

1.1.1.1.1 	Cranking ignition angle calculation

1.1.1.1.1.1 	First ignition angle at engine stopped (LV_ES)

1.1.1.1.1.2 	Ignition angle at start (LV_ST)

1.1.1.1.2 	Nominal ignition angle (out of start) calculation

1.1.1.1.2.1 	Basic ignition angle without gradient limitation ( IGA_BAS )

1.1.1.1.2.2 	Global ignition angle correction ( IGA_ADD_COR )

1.1.1.1.2.3 	Ignition angle out of start without torque intervention ( IGA_CYL_(CYL( )

1.1.1.2 	Ignition angle application ( IGA_IGC_(CYL(, IGA_IGC_SAM)

1.2 	Calculation of ignition angle corrections

1.2.1 	Dynamic ignition angle correction in idle ( IGA_DYN_COR_IS )

1.2.2 	Air and coolant temperatures correction out of idle ( IGA_TIA_TCO )

1.2.3 	Catalyst heating correction ( IGA_CH )

1.2.4 	Instationary correction ( IGA_TRA_KNK )

1.2.5 	Anti - jerk correction ( IGA_AJ )

1.2.6 	Trailing throttle correction ( IGA_PU_PUC )

1.2.7 	Tuning correction ( IGA_AS_(CYL( )

1.3 	Calculation of basic ignition angle

1.3.1 	Basic ignition angle at start ( IGA_ST )

1.3.2 	Basic ignition angle out of start ( IGAB )

1.3.3 	Basic ignition angle with gradient limitation ( IGA_BAS_LGRD )

1.3.3.1 	Engine operating states without gradient limitation for ignition angle.

1.3.3.	2 Gradient limitation for ignition angle at intercept function ( LV_INF )

1.3.3.3 	Re-start fuel feed ( LV_REAC ) at part load ( LV_PUC ( LV_PL )

1.3.3.4 	Re-start fuel feed ( LV_REAC ) at idle ( LV_PUC ( ( LV_PU )( LV_IS )

1.3.3.5 	Gradient limitation for ignition angle with anti-jerk correction ( LV_AJ_ACT )

1.3.3.6 	Gradient limitation for ignition angle with instationary correction (LV_TRA_KNK_ACT)

1.3.3.7 	Gradient limitation for ignition angle with knock detected

1.3.3.8 	Gradient limitation for transition Part Load (PL) -> Idle Speed (IS)

1.3.3.9 	General gradient limitation for ignition angle

1.4 	Knock control

1.4.1 	General - Knock correction ( IGA_KNK_(CYL( )

1.4.1.1 	Conditions for knock control in normal operation or in limp home

1.4.1.2 	Ignition angle correction out of knock detection area

1.4.1.3 	Ignition angle knock correction mean value ( IGA_MV_KNK )

1.4.1.4 	Relative knock corrections limitation

1.4.1.5 	Absolute knock corrections limitation

1.4.2 	Knock control in normal operation

1.4.3 	Knock control in limp home

1.4.4 	Knock adaptation

Index	Page

:

C

C_DRI_TPS_GRD_MIN_AJ

def	26

C_IGA_AD_DIF_MAX

def	50

C_IGA_AS_[CYL]

def	32

C_IGA_DIF_MAX_MIN_KNK

def	48

C_IGA_FAC_2_AJ

def	26

C_IGA_FAC_3_AJ

def	26

C_IGA_INC_AD

def	53

C_IGA_LGRD_1

def	45

use	36, 37, 39

C_IGA_LGRD_2

def	45

use	37, 39, 42

C_IGA_LGRD_3

def	45

use	37, 39, 46

C_IGA_LGRD_CH

def	19

C_IGA_LGRD_PL_IS

def	43

C_IGA_LGRD_x

use	27

C_IGA_MAF_LGRD

def	45

C_IGA_N_DIF_FAC_IS

def	16

C_IGA_N_LGRD

def	45

C_N_GRD_MIN

use	27

C_N_MAX_AJ

def	26

C_N_MAX_INF

use	27

C_N_MIN_AJ

def	26

C_N_MIN_DHP

def	31

C_N_THD_T_MES_AJ

def	26

C_SUM_TRIG_AJ

def	26

C_T_MAX_AJ

def	26

C_T_MAX_GRD_2_ST_AJ

def	26

C_T_TPS_GRD_MIN_AJ

def	26

C_TCO_MIN_AJ

def	26

C_TPS_GRD_BOL_RPL

def	38

use	20

C_TPS_GRD_MIN_AJ

def	26

C_VS_MAX_AJ

def	26

C_VS_MIN_AJ

def	26

I

ID_IGA_AD_[CYL]__N_KNK__MAF_KNK

def	53

use	49

ID_IGA_CYCNR_TRA_KNK(_AT)__N_32

def	21

ID_IGA_DEC_1_KNK__N_KNK

def	50

ID_IGA_DEC_2_KNK__N_KNK

def	50

ID_IGA_INC_KNK__N_KNK

def	50

ID_IGA_LGRD_END_AJ__N_32

def	41

use	22

ID_IGA_LGRD_RPL__N_32

def	38

ID_IGA_LGRD_ST_AJ__N_32

def	26

ID_IGA_MIN_PL__TCO

def	14

ID_IGA_RPL__N_32__TCO

def	38

use	20

ID_IGA_T_CH__TCO_ST

use	18

ID_IGA_TCO_LGRD_PU(_AT)__TCO

def	31

ID_IGA_TPS_GRD_TRA__N_32

def	21

use	39

ID_IGA_TRA_KNK(_AT)__N_32__MAF

def	21

ID_MAF_MIN_AD_KNK__N_32

def	53

IGA_ADD_COR

def	11

IGA_AJ

def	22

use	11, 41

IGA_AS_[CYL]

def	32

use	11

IGA_BAS

def	11

use	35, 36, 37, 39, 41, 42, 43, 44

IGA_BAS_LGRD

def	35

use	11

IGA_CAT

use	11

IGA_CH

def	18

use	46

IGA_CYL_[CYL]

def	11

IGA_DYN_COR_IS

def	15

use	11

IGA_EGR

use	11

IGA_IGC_[CYL]

def	11

IGA_IGC_SAM

def	11

IGA_KNK_[CYL]

def	46

use	11, 49

IGA_MV_KNK

def	46

use	51

IGA_PU_PUC

def	27

use	11

IGA_SAM

def	11

IGA_ST

def	33

use	11

IGA_TIA_TCO

def	17

use	11

IGA_TQR

use	11

IGA_TRA_KNK

def	20

use	11, 37, 39, 42

IGAB

def	34

use	11

IP_IGA_ACCIN_PUC(_AT)__N

def	31

IP_IGA_AJ__N_32__MAF

def	26

IP_IGA_AST__N_DIF_COR

def	16

IP_IGA_CH__N_32__MAF

def	19

IP_IGA_CH_IS__N_32__MAF

def	19

IP_IGA_FAC_IS(_AT)__TCO

def	16

IP_IGA_LGRD_PU(_AT)__N_32__MAF_MMV

def	31

IP_IGA_LGRD_RIS__N_GRD

def	40

IP_IGA_MAX_KNK__N_32__MAF

def	48

IP_IGA_MAX_PUC__N

def	31

IP_IGA_N_DIF_IS(_AT)__N_DIF_COR

def	16

IP_IGA_N_MAF__N_32__MAF

def	17

IP_IGA_PU(_AT)__N__TCO

def	31

IP_IGA_PUC(_AT)__N

def	31

IP_IGA_ST__N__TCO_ST

def	33

IP_IGA_TCO_CH__TCO__T_AST

def	19

IP_IGA_TCO_CH_IS__TCO__T_AST

def	19

IP_IGA_TCO_FAC_KNK__TCO

def	48

IP_IGA_TCO_IS__TCO

def	34

IP_IGA_TRA_FAC(_AT)__TIA

def	21

IP_IGAB__N__MAF

def	34

IP_IGAB_INF__TCO

def	36

IP_IGAB_IS__N__MAF

def	34

IP_N_ACCIN_MIN_PUC(_AT)__TCO

use	27

IP_N_MIN_PUC(_AT)__TCO

use	27

IP_T_MES_GRD_1_ST_AJ__N_32

def	26

IP_T_MES_GRD_2_ST_AJ__N_32

def	26

IP_T_MES_GRD_END_AJ__N_32

def	26

IP_TIA_TCO_FAC(_AT)__TIA__TCO

def	17

ISAPWM_D_IS

use	27

ISAPWM_DHP

use	27

K

KNK_INT_CYL_[CYL]

use	43, 49

KNKS_[CYL]

use	49

L

LV_AJ_ACT

def	22

use	41

LV_CAM_ERR

use	22, 51

LV_CAM_ERR_LIH

use	46

LV_CRK_ERR

use	22, 51

LV_CRK_ERR_LIH

use	46

LV_CT

use	27

LV_CYC_WUP_KNK

def	51

LV_DRI

use	22

LV_DUR_IGC_[CYL]_ERR

use	22

LV_ES

use	11, 33

LV_IGA_AD_ACT

def	51

LV_IGA_ADJ_TQR

use	46, 49, 51

LV_IGA_AST

use	15, 35

LV_IGA_CH

use	18, 46, 51

LV_INF

use	36

LV_IS

use	11, 15, 18, 34, 39, 43, 51

LV_ISA_1_ERR

use	51

LV_ISA_2_ERR

use	51

LV_ISAPWM_IS_ACT

use	15, 35

LV_IV_[CYL]_ERR

use	22

LV_KNK_1_ERR

use	46, 51

LV_KNK_2_ERR

use	46, 51

LV_KNK_ACT

use	46, 49, 51

LV_LSH_UP_1_ERR

use	51

LV_LSH_UP_2_ERR

use	51

LV_MAF_ERR

use	51

LV_N_GRD_INF

use	36

LV_N_GRD_MAX_KNK

use	51

LV_PL

use	11, 20, 22, 27, 37, 39, 43

LV_PU

use	11, 27, 39

LV_PU_PUC_TRA_FAST

use	27

LV_PUC

use	11, 20, 27, 35, 37, 39

LV_REAC

use	20, 37, 39

LV_RLY_ACCOUT

use	27

LV_SCC_TQR

use	51

LV_ST

use	11, 15, 33, 35

LV_STATE_A_MIS

use	22, 51

LV_STATE_B_MIS

use	22, 51

LV_SYN_ENG

use	11

LV_TCO_ERR

use	51

LV_TIA_ERR

use	51

LV_TPS_ERR

use	51

LV_TPS_FL

use	18, 46, 51

LV_TPS_GRD_TRA_KNK

use	51

LV_TRA_KNK_ACT

def	20

use	37, 39, 42, 46, 49

LV_TRA_TPS_GRD_MIN_AJ

def	22

LV_VLS_LIM_1_ERR

use	51

LV_VLS_LIM_2_ERR

use	51

M

MAF

use	17, 18, 20, 22, 34, 44

MAF_KNK

use	49, 51

MAF_MMV

use	27

N

N

use	22, 27, 33, 34, 44

N_32

use	17, 18, 20, 22, 27, 34, 37, 39, 41, 51

N_DIF_COR

use	15

N_GRD

use	27, 39

N_KNK

use	49, 51

NC_CYL_NO

def	48

NC_INI_IGA

def	14

NL_THD_KNK_[CYL]

use	49

S

SUM_TRIG_AJ

def	22

T

T_AST

use	18

T_MES_GRD_AJ

def	22

T_SEG

use	22

TCO

use	15, 17, 18, 20, 22, 27, 34, 36, 37

TCO_ST

use	33

TIA

use	17, 20

TPS_GRD

use	20, 22, 37, 39

V

VS

use	15, 22

General

Total formulas

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_BAS | V | 0...FFH | -23,625...72 | 0,375 | °CRK |
| Basic ignition angle calculation without gradient limitation. |
| IGA_ADD_COR | - | 0...FFH | -23,625...72 | 0,375 | °CRK |
| Global ignition angle correction. |
| IGA_CYL_[CYL] | V | 0...FFH | 72...-23,625 | 0,375 | °CRK |
| Individual ignition angle calculation without torque intervention. |
| IGA_SAM | V | 0...FFH | 72...-23,625 | 0,375 | °CRK |
| Individual ignition angle calculation without torque intervention updated each segment. |
| IGA_IGC_[CYL] | V | 0...FFH | 72...-23,625 | 0,375 | °CRK |
| Individual applied ignition angle with torque intervention. |
| IGA_IGC_SAM | V | 0...FFH | 72...-23,625 | 0,375 | °CRK |
| Individual applied ignition angle with torque intervention updated each segment. |

Input data:

| LV_SYN_ENG | LV_ES | LV_ST | IGA_ST |
| --- | --- | --- | --- |
| IGA_KNK_[CYL] | IGA_AS_[CYL] | IGAB | IGA_DYN_COR_IS |
| IGA_TIA_TCO | IGA_CAT | IGA_EGR | IGA_TQR |
| IGA_TRA_KNK | IGA_AJ | IGA_PU_PUC | IGA_BAS_LGRD |
| LV_IS | LV_PU | LV_PUC | LV_PL |

Ignition angle calculation ( IGA_CYL_(CYL] , IGA_SAM )

Cranking ignition angle calculation

First ignition angle at engine stopped (LV_ES)

If	LV_SYN_ENG = 1		(synchronisation effective)

and	engine stopped (LV_ES)

then	IGA_CYL_(CYL(  =  NC_INI_IGA

Ignition angle at start (LV_ST)

IGA_CYL_(CYL(	=	IGA_ST		Cranking ignition angle.

+	IGA_KNK_(CYL		Knock correction.

+	IGA_AS_(CYL(		Application system intervention.

Application recurrence : Segment

Nominal ignition angle (out of start) calculation

Basic ignition angle without gradient limitation ( IGA_BAS )

IGA_BAS	=	IGAB				Basic ignition angle.

+	min (	IGA_ADD_COR,	Global ignition angle correction.

IGA_AJ)			Anti-jerk correction.

Application recurrence : Segment

Global ignition angle correction ( IGA_ADD_COR )

IGA_ADD_COR	=	IGA_DYN_COR_IS		Dynamic correction in idle 										(LV_IS)

+	IGA_TIA_TCO		Air and coolant temperatures 									correction.

+	IGA_CH			Catalyst heating correction.

+	IGA_EGR			EGR correction.

+	IGA_TRA_KNK		Instationary correction.

+	IGA_PU_PUC			Trailing throttle correction 										(LV_PU / LV_PUC)

Application recurrence : Segment

Ignition angle out of start without torque intervention ( IGA_CYL_(CYL( )

IGA_CYL_(CYL(	=	IGA_BAS_LGRD	Basic ignition angle with 										gradient limitation.

+	IGA_KNK_(CYL(		Knock correction.

+	IGA_AS_(CYL(		Application system 											intervention.

Application recurrence : Segment

See next page for illustration.

Remark :

The basic ignition angle with gradient limitation IGA_BAS_LGRD is described in chapter 1.1.2.

Ignition angle application ( IGA_IGC_(CYL(, IGA_IGC_SAM)

General information:

The algorithm for torque intervention (GS, ASR or MSR) uses ignition angle control.

It provides IGA_IGC_(CYL( with IGA_CYL_(CYL( from applicative layer and IGA_TQR through a torque intervention model as input data.

The minimum ignition angle is limited to ID_IGA_MIN_PL__TCO in part load (LV_PL).

Description:

Formula section:

If		LV_PL = 1

then

If	IGA_IGC_[CYL] (= ID_IGA_MIN_PL__TCO

then	IGA_IGC_[CYL] = ID_IGA_MIN_PL__TCO

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| ID_IGA_MIN_PL__TCO | 8 | 0...FFH | 72 ...-23,625 | 0,375 | °CRK |
|  | Ignition angle limitation in retard direction in part load. |
| NC_INI_IGA | 1 | 0...FFH | 72 ...-23,625 | 0,375 | °CRK |
| First ignition angle following synchronisation in engine stopped (LV_ES) - Non adjustable calibration. |

Applicative Value :

NC_INI_IGA = 50H = 6,375 °CRK

Calculation of ignition angle corrections

Dynamic ignition angle correction in idle ( IGA_DYN_COR_IS )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_DYN_COR_IS | V | 0...FFH | -48...47,625 | 0,375 | °CRK |
| Dynamic ignition angle correction in idle (LV_IS). |

Input data:

| LV_IS | LV_ST | LV_IGA_AST | LV_ISAPWM_IS_ACT |
| --- | --- | --- | --- |
| N_DIF_COR | TCO | VS |

FUNCTION DESCRIPTION:

General information:

This ignition angle intervention is depending on the engine speed deviation from the nominal idle speed.

The calculation is made depending on the state of the idle speed regulation. As soon as the regulation is active, the dynamic ignition angle correction is applied with a factor which depends on VS and N_DIF_COR. It also prevents excessive overshooting when a transition from start (LV_ST) to idle (LV_IS) appeared with engine speed above nominal idle speed.

Application recurrence : Segment

Formula section:

- If		engine operating state idle (LV_IS) active

and	LV_ISAPWM_IS_ACT = 1 (Active)	(idle speed regulation active)

then

If 	(  VS = 0  or  N_DIF_COR > 0  )

then

IGA_DYN_COR_IS  = IP_IGA_N_DIF_IS(_AT)__N_DIF_COR * IP_IGA_FAC_IS(_AT)__TCO

else

IGA_DYN_COR_IS   =   IP_IGA_N_DIF_IS__N_DIF_COR * IP_IGA_FAC_IS(_AT)__TCO

* C_IGA_N_DIF_FAC_IS

else

If	engine operating state idle (LV_IS) active

and	LV_IGA_AST = 1 (Active)	(ignition angle intervention due to post

start function)

then

IGA_DYN_COR_IS = IP_IGA_AST__N_DIF_COR

else

IGA_DYN_COR_IS = 0

Endif.

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_AST__N_DIF_COR | 4 | 0...FFH | -48...47,625 | 0,375 | °CRK |
|  | Dynamic ignition angle correction for post start function (LV_IGA_AST). |
| IP_IGA_N_DIF_IS(_AT)__N_DIF_COR | 12 | 0...FFH | -48...47,625 | 0,375 | °CRK |
|  | Dynamic ignition angle correction for idle speed stabilisation (LV_ISAPWM_IS_ACT). |
| IP_IGA_FAC_IS(_AT)__TCO | 4 | 0...FFH | 0...0,996 | 1 / 256 | - |
|  | Weighting factor versus coolant temperature for dynamic ignition angle correction. |
| C_IGA_N_DIF_FAC_IS | 1 | 0...FFH | 0...0,996 | 1/256 | - |
| Dynamic angle correction in case of vehicle running |

Air and coolant temperatures correction out of idle ( IGA_TIA_TCO )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_TIA_TCO | V | 0...FFH | -48...47,625 | 0,375 | °CRK |
| Ignition angle correction versus temperatures out of idle. |

Input data:

| TIA | TCO | N_32 | MAF |
| --- | --- | --- | --- |

FUNCTION DESCRIPTION:

General information:

The basic ignition angle out of idle is adjusted versus ambient conditions.

It is increased for low coolant temperature and decreased for high air temperature when engine is warm.

Application recurrence : 720 °CRK

Formula section:

IGA_TIA_TCO = IP_TIA_TCO_FAC(_AT)__TIA__TCO * IP_IGA_N_MAF__N_32__MAF

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_TIA_TCO_FAC(_AT)__TIA__TCO | 6 x 6 | 00...FFH | -1...0,992 | 7,8125E-3 | - |
|  | Weighting factor versus temperatures for ignition angle correction IGA_TIA_TCO. |
| IP_IGA_N_MAF__N_32__MAF | 8 x 6 | 0...FFH | -48...47,625 | 0,375 | °CRK |
|  | Basic ignition angle correction versus temperatures out of idle. |

Catalyst heating correction ( IGA_CH )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_CH | V | 0...FFH | -48...47,625 | 0,375 | °CRK |
| Catalyst heating ignition angle correction. |

Input data:

| LV_IGA_CH | LV_IS | N_32 | MAF |
| --- | --- | --- | --- |
| TCO | T_AST | LV_TPS_FL | ID_IGA_T_CH__TCO_ST |

FUNCTION DESCRIPTION:

General information:

The basic ignition angle out of start is adjusted in order to improve catalyst heating during warm-up. Thus, the catalyst reaches its service temperature quicklier and earlier its own efficiency.

Application recurrence :

- segment :		if LV_IGA_CH = 1 (Active). IGA_CH is performed without gradient 				limitation.

- 720 °CRK :	if LV_IGA_CH deactivated. IGA_CH is reset with a gradient limitation.

Formula section:

If		LV_IGA_CH = 1 (Active)

then

If		engine operating state idle speed (LV_IS) active

then

IGA_CH = IP_IGA_CH_IS__N_32__MAF * IP_IGA_TCO_CH_IS__TCO__T_AST

else

IGA_CH = IP_IGA_CH__N_32__MAF * IP_IGA_TCO_CH__TCO__T_AST

(out of idle)

Remark :

- When the duration ID_IGA_T_CH__TCO_ST has elapsed, the catalyst heating ignition 	angle correction is disabled using a gradient limitation C_IGA_LGRD_CH.

- The ignition angle intervention for catalyst heating function is stopped when full load 	(LV_TPS_FL) is required.

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_CH_IS__N_32__MAF | 8 ( 8 | 0...FFH | -48...47,625 | 0,375 | °CRK |
|  | Catalyst heating ignition angle correction versus engine speed in idle (LV_IS). |
| IP_IGA_TCO_CH_IS__TCO__T_AST | 8 x 8 | 0...FFH | 0...0,997 | 3,895E-3 | - |
|  | Catalyst heating ignition angle factor versus coolant temperature in idle (LV_IS). |
| IP_IGA_CH__N_32__MAF | 8 x 8 | 0...FFH | -48...47,625 | 0,375 | °CRK |
|  | Catalyst heating ignition angle correction versus engine speed out of idle. |
| IP_IGA_TCO_CH__TCO__T_AST | 8 x 8 | 0...FFH | 0...0,997 | 3,895E-3 | - |
|  | Catalyst heating ignition angle factor versus coolant temperature out of idle. |
| C_IGA_LGRD_CH | 1 | 01H...7FFFH | 0,00146...48 | 48 / 32767 | °CRK |
| Gradient limitation for catalyst heating ignition angle correction disabling. |

Instationary correction ( IGA_TRA_KNK )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_TRA_KNK | V | 0...80H | -48...0 | 0,375 | °CRK |
| Ignition angle for instationary correction. |
| LV_TRA_KNK_ACT | V | 0...01H | 0...1 | 1 | - |
| Boolean information for ignition instationary correction requested - ( Passive / Active ). |

Input data:

| LV_PL | N_32 | MAF | TIA |
| --- | --- | --- | --- |
| LV_PUC | TCO | TPS_GRD | C_TPS_GRD_BOL_RPL |
| LV_REAC | ID_IGA_RPL__N_32__TCO |

FUNCTION DESCRIPTION:

General information:

In order to prevent knock during strong acceleration, an ignition angle correction is applied to the nominal ignition angle out of start.

Application recurrence : Segment.

Application conditions:

- Preliminary :

If		LV_PUC ( LV_PL	( restart fuel feed at part load - LV_REAC = 0 ( 1 )

and	TPS_GRD < C_TPS_GRD_BOL_RPL		( smooth acceleration )

and	IGA_TRA_KNK< ID_IGA_RPL__N_32__TCO

or

engine operating state part load (LV_PL) active

and	TPS_GRD ( ID_IGA_TPS_GRD_TRA__N_32	( strong acceleration )

then	LV_TRA_KNK_ACT = 1 (Active)

else		LV_TRA_KNK_ACT = 0 (Passive)

Endif.

Formula section:

If	LV_TRA_KNK_ACT = 1 (Active)

then

IGA_TRA_KNK = ID_IGA_TRA_KNK(_AT)__N_32__MAF * IP_IGA_TRA_FAC(_AT)__TIA

and	as soon as IGA_TRA_KNKn ( IGA_TRA_KNKn-1,

IGA_TRA_KNK remains unmodified during

ID_IGA_CYCNR_TRA_KNK__N_32__MAF x segments.

else	IGA_TRA_KNK = 0.

Description:

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| ID_IGA_TPS_GRD_TRA__N_32 | 4 | 0...FFH | 0...2988 | 2988 / 256 | °TPS/sec |
|  | TPS_GRD threshold for ignition angle with instationary correction detection. |
| ID_IGA_TRA_KNK(_AT)__N_32__MAF | 4 x 4 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Ignition angle for instationary correction versus engine operating point. |
| IP_IGA_TRA_FAC(_AT)__TIA | 4 | 0...FFH | 0...0,996 | 1 / 256 | - |
|  | Weighting factor versus air temperature for ignition angle during instationary correction. |
| ID_IGA_CYCNR_TRA_KNK(_AT)__N_32 | 4 | 0...FFH | 0...255 | 1 | - |
|  | Duration of ignition angle during instationary correction - ( x Segment ). |

Anti - jerk correction ( IGA_AJ )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_AJ | V | 80H...7FH | -48...47,625 | 0,375 | °CRK |
| Anti - jerk ignition angle correction. |
| T_MES_GRD_AJ | V | 8000...7FFFH | -0,125...0,125 | 3,814E-5 | - |
| Segment time ratio for activation conditions of the anti - jerk function. |
| SUM_TRIG_AJ | V | 0...0AH | 0...10 | 1 | - |
| Triggering counter for successive ignition angle intervention. |
| LV_TRA_TPS_GRD_MIN_AJ | V | 0...01H | 0...1 | 1 | - |
| Boolean corresponding to TPS gradient conditions for activation of the anti - jerk function (passive / active). |
| LV_AJ_ACT | V | 0...01H | 0...1 | 1 | - |
| Boolean for ignition angle intervention when anti - jerk function is required (passive / active). |

Input data:

| N_32 | TPS_GRD | T_SEG | VS |
| --- | --- | --- | --- |
| N | LV_DRI | LV_PL | LV_IV_[CYL]_ERR |
| MAF | LV_STATE_A_MIS | LV_DUR_IGC_[CYL]_ERR | LV_CRK_ERR |
| TCO | LV_STATE_B_MIS | ID_IGA_LGRD_END_AJ__N_32 | LV_CAM_ERR |

FUNCTION DESCRIPTION:

General information:

Due to sudden transition from an engine operating point in low part load to wide open throttle, jerking can occur in the lower engine speed range during acceleration.

These jerks have to be suppressed, which can be achieved by a selective torque reduction. Thus ignition is retarded during the positive half - wave of the engine speed wave.

1 - Segment time ratio T_MES_GRD_AJ :

In order to start ignition intervention, “jerk” must be previously detected using the segment time ratio T_MES_GRD_AJ.

It is calculated using the corresponding segment periods :

T_REV_ACT= ( T_SEGn + T_SEGn-1)

T_REV_LAST = ( T_SEGn-2 + T_SEGn-3 )

If	N_32 ( C_N_THD_T_MES_AJ

then	T_MES_GRD_AJ = ( T_SEGn - T_SEGn-1 ) / T_SEGn

else	T_MES_GRD_AJ = ( T_REV_ACT - T_REV_LAST ) / T_REV_ACT

2 - TPS gradient condition LV_TRA_TPS_GRD_MIN_AJ :

In order to start ignition intervention for first triggering, a condition on the gradient of the throttle position sensor must be provided.

It is defined using the following algorithm :

If		TPS_GRD > C_TPS_GRD_MIN_AJ			( LV_DRI = - )

or	TPS_GRD > C_DRI_TPS_GRD_MIN_AJ		( LV_DRI = DRI )

then		LV_TRA_TPS_GRD_MIN_AJ = 1 (Active)

and	C_T_TPS_GRD_MIN_AJ is started.

If		C_T_TPS_GRD_MIN_AJ has elapsed

or	anti - jerk deactivation conditions are fulfilled

then		LV_TRA_TPS_GRD_MIN_AJ = 0 (Passive)

Application conditions:

1 - Anti - jerk function :

Activation :

Engine operating state part load (LV_PL)

and	TCO > C_TCO_MIN_AJ

and	C_N_MIN_AJ < N_32 < C_N_MAX_AJ

and	C_VS_MIN_AJ < VS < C_VS_MAX_AJ

and	the following diagnosis errors are not permitted :

LV_CRK_ERR = 0			(crankshaft sensor)

and	LV_CAM_ERR = 0			(camshaft sensor)

and	LV_DUR_IGC_(CYL(_ERR = 0	(ignition coils)

and	LV_IV_(CYL(_ERR = 0		(injector valves)

and	LV_STATE_A_MIS = 0		(misfire status - error CARB A)

and	LV_STATE_B_MIS = 0		(misfire status - error CARB B)

Deactivation :

T_MES_GRD_AJ > IP_T_MES_GRD_END_AJ__N_32

or	timer C_T_MAX_AJ has elapsed

or	timer C_T_MAX_GRD_2_ST_AJ has elapsed.

2 - Ignition intervention - First triggering :

Activation :

If		LV_TRA_TPS_GRD_MIN_AJ = 1 (active)

and	T_MES_GRD_AJ < IP_T_MES_GRD_1_ST_AJ__N_32

and	T_MES_GRD_AJ ( IP_T_MES_GRD_END_AJ__N_32

then		SUM_TRIG_AJ = 1		(initialisation)

and	LV_AJ_ACT = 1 (active)	(ignition angle intervention takes 								 	place)

and	C_T_MAX_GRD_2_ST_AJ	(timer initialisation)

and	C_T_MAX_AJ			(timer initialisation)

Remark :		C_T_MAX_AJ < C_T_MAX_GRD_2_ST_AJ

3 - Ignition intervention - Second triggering and further :

Activation :

If		1 < SUM_TRIG_AJ ( C_SUM_TRIG_AJ

and	T_MES_GRD_AJ < IP_T_MES_GRD_2_ST_AJ__N_32

and	T_MES_GRD_AJ ( IP_T_MES_GRD_END_AJ__N_32

then		LV_AJ_ACT = 1 (Active)(ignition angle intervention take place)

and	SUM_TRIG_AJi = SUM_TRIG_AJ i-1 + 1

and	C_T_MAX_AJ initialisation.

Formula section:

First triggering :

If		LV_AJ_ACT = 1 (Active)

and	SUM_TRIG_AJ = 1

then		IGA_AJ = IP_IGA_AJ__N_32__MAF

Second triggering :

If		LV_AJ_ACT = 1 (Active)

and	SUM_TRIG_AJ = 2

then		IGA_AJ = IP_IGA_AJ__N_32__MAF * C_IGA_FAC_2_AJ

Third and further triggering :

If		LV_AJ_ACT = 1 (Active)

and	2 < SUM_TRIG_AJ ( C_SUM_TRIG_AJ

then		IGA_AJ = IP_IGA_AJ__N_32__MAF * C_IGA_FAC_3_AJ

Remark :

The ignition angle retard adjustment is applied with a gradient limitation ID_IGA_LGRD_ST_AJ__N_32. The return to the nominal ignition angle at the end of the correction is performed with a gradient limitation ID_IGA_LGRD_END_AJ__N_32 (refer to the chapter “ Ignition angle gradient limitation “)

Description:

1 - Ignition intervention description :

2 - Timer description :

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_AJ__N_32__MAF | 8 x 6 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Basic anti-jerk ignition angle correction. |
| ID_IGA_LGRD_ST_AJ__N_32 | 8 | 01...FFH | 0,375...95,625 | 0,375 | °CRK |
|  | Gradient limitation to reach the anti-jerk ignition angle correction (x Segment). |
| IP_T_MES_GRD_1_ST_AJ__N_32 | 10 | 0...8000H | -0,125...0 | 3,8E-6 | msec/mse |
|  | T_MES_GRD_AJ threshold for first ignition intervention triggering. |
| IP_T_MES_GRD_2_ST_AJ__N_32 | 10 | 0...8000H | -0,125...0 | 3,8E-6 | msec/mse |
|  | T_MES_GRD_AJ threshold for second and further ignition intervention triggering. |
| IP_T_MES_GRD_END_AJ__N_32 | 10 | 0...8000H | -0,125...0 | 3,8E-6 | msec/mse |
|  | T_MES_GRD_AJ threshold to cancel anti-jerk ignition angle correction. |
| C_N_THD_T_MES_AJ | 1 | 0...FFH | 0...8160 | 32 | rpm |
| Engine speed threshold for calculation of T_MES_GRD_AJ. |
| C_TCO_MIN_AJ | 1 | 0...FEH | -48...142,5 | 0,75 | °C |
| Minimum coolant temperature threshold for application condition of anti-jerk function. |
| C_N_MIN_AJ | 1 | 0...FFH | 0...8160 | 32 | rpm |
| Minimum engine speed threshold for application condition of anti-jerk function. |
| C_N_MAX_AJ | 1 | 0...FFH | 0...8160 | 32 | rpm |
| Maximum engine speed threshold for application condition of anti-jerk function. |
| C_VS_MIN_AJ | 1 | 0...FFH | 0...255 | 1 | km/h |
| Minimum vehicle speed threshold for application condition of anti-jerk function. |
| C_VS_MAX_AJ | 1 | 0...FFH | 0...255 | 1 | km/h |
| Maximum vehicle speed threshold for application condition of anti-jerk function. |
| C_TPS_GRD_MIN_AJ | 1 | 0...FFH | 0...2988 | 11,72 | °TPS/sec |
| Minimum TPS_GRD threshold for application condition of anti-jerk function. (DRIVE not engaged). |
| C_DRI_TPS_GRD_MIN_AJ | 1 | 0...FFH | 0...2988 | 11,72 | °TPS/sec |
| Minimum TPS_GRD threshold for application condition of anti-jerk function. (DRIVE engaged). |
| C_IGA_FAC_2_AJ | 1 | 00...FFH | 0...1,000 | 3,906E-3 | - |
| Weighting factor for second ignition intervention triggering. |
| C_IGA_FAC_3_AJ | 1 | 00...FFH | 0...1,000 | 3,906E-3 | - |
| Weighting factor for third and further ignition intervention triggering. |
| C_T_MAX_AJ | 1 | 01...FFH | 0,01...25,5 | 0,01 | sec |
| Maximum duration of the ignition intervention. |
| C_T_MAX_GRD_2_ST_AJ | 1 | 01...FFFFH | 0,01...655,35 | 0,01 | sec |
| Maximum duration of the anti-jerk function. |
| C_T_TPS_GRD_MIN_AJ | 1 | 01...FFH | 0,1...25,5 | 0,1 | sec |
| Time exceeding the TPS_GRD threshold for activation and deactivation of the anti-jerk function. |
| C_SUM_TRIG_AJ | 1 | 01...0AH | 1...10 | 1 | - |
| Number of anti-jerk ignition angle intervention triggering. |

Trailing throttle correction ( IGA_PU_PUC )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_PU_PUC | V | 0...80H | -48...0 | 0,375 | °CRK |
| Trailing throttle ignition angle correction. |

Input data:

| LV_PL | LV_PU | LV_PU_PUC_TRA_FAST | LV_PUC |
| --- | --- | --- | --- |
| LV_CT | C_IGA_LGRD_x | LV_RLY_ACCOUT | TCO |
| MAF_MMV | N_GRD | ISAPWM_D_IS | ISAPWM_DHP |
| N_32 | N | IP_N_MIN_PUC(_AT)__TCO | C_N_MAX_INF |
| IP_N_ACCIN_MIN_PUC(_AT)__TCO | C_N_GRD_MIN |

FUNCTION DESCRIPTION:

General information:

A preliminary check is made on the type of deceleration ( LV_PU_PUC_TRA_FAST ) at the transition from engine operating state in part load ( LV_PL ) to trailing throttle ( LV_PU ) in order to define the right ignition angle correction.

- In case of fast deceleration ( LV_PU_PUC_TRA_FAST = 1 (Active) ), the fuel injection is switched off immediately and the nominal ignition angle out of start is adjusted with IGA_PU_PUCin order to get the lowest possible engine torque to avoid a torque jump.

- In case of slow deceleration ( LV_PU_PUC_TRA_FAST = 0 (Passive) ), trailing throttle fuel cut-off is delayed and the nominal ignition angle correction out of start is adjusted with IGA_PU_PUCin order to prevent engine acceleration when shifting below high load.

Application recurrence : Segment.

Formula section:

- IGA_PU_PUC formula:

If 	LV_PU = 0

and LV_PUC = 0

then

IGA_PU_PUC = 0

else

if 	LV_PUC = 1

then

if 	LV_PU_PUC_TRA_FAST = 1

then

IGA_PU_PUC = IP_IGA_MAX_PUC__N

else

IGA_PU_PUC = IP_IGA_PUC(_AT)__N or 							IP_IGA_ACCIN_PUC(_AT)__N

else

if 	LV_PU = 1

then

IGA_PU_PUC = IP_IGA_PU__N__TCO

using gradient limitation in the decreasing direction					IP_IGA_LGRD_PU(_AT)__N_32__MAF_MMV + ID_IGA_TCO_LGRD_PU__TCO

and

Exit conditions from LV_PU to LV_PUC are tested

- Exit conditions from LV_PU to LV_PUC :

If		LV_CT = 1

and	N_32 ( IP_N_MIN_PUC(_AT)__TCO + Hysteresis	   ( (LV_RLY_ACCOUT = 0)

or N_32( IP_N_ACCIN_MIN_PUC(_AT)__TCO + Hyst.

( (LV_RLY_ACCOUT = 1)

and	ISAPWM_D_IS= 0	( (derivative term from idle speed controller inactive)

and	N_32( C_N_MAX_INF

or  ( N_32 < C_N_MAX_INF  and  N_GRD ( C_N_GRD_MIN )

then

If		LV_PU_PUC_TRA_FAST = 1 (Active) ( (fast deceleration)

then

LV_PUC = 1	(  (trailing throttle fuel cut-off immediately)

and	IGA_PU_PUC = IP_IGA_MAX_PUC__N ( (without gradient limitation)

else ( (slow deceleration)

If	N_32 < C_N_MIN_DHP

or	N_32 ( C_N_MIN_DHP

and	ISAPWM_DHP = 0 ( (dashpot function inactive)

and	IGA_PU_PUC = IP_IGA_PUC(_AT)__N 							or IGA_PU_PUC=IP_IGA_ACCIN_PUC(_AT)__N								(LV_RLY_ACCOUT=1)
		then

LV_PUC = 1

else

LV_PU = 1

until	IGA_PU_PUC = IP_IGA_PUC(_AT)__N

or	IGA_PU_PUC = IP_IGA_ACCIN_PUC(_AT)__N  (  (LV_RLY_ACCOUT = 1)

using  IP_IGA_LGRD_PU(_AT)__N_32__MAF_MMV + ID_IGA_TCO_LGRD_PU__TCO 		gradient limitation

else

LV_PU = 1

and	IGA_PU_PUC = IP_IGA_PU__N__TCO

using  IP_IGA_LGRD_PU(_AT)__N_32__MAF_MMV + ID_IGA_TCO_LGRD_PU__TCO 		gradient limitation in the decreasing direction

Description:

Remark :

- Tuning information :

The gradient limitation used for ignition angle correction (IGA_PU_PUC) in trailing throttle (LV_PU) or trailing throttle fuel cut-off (LV_PUC) must be lower than the general gradient limitation used for the nominal ignition angle out of start (IGA_BAS) :

(IP_IGA_LGRD_PU(_AT)__N_32__MAF_MMV + ID_IGA_TCO_LGRD_PU__TCO) 
   (  C_IGA_LGRD_x

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_PU(_AT)__N__TCO | 4 x 4 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Target ignition angle in case of slow deceleration in trailing throttle (LV_PU). |
| ID_IGA_TCO_LGRD_PU(_AT)__TCO | 4 | 01...7FFFH | 0,0146...48 | 48 / 32767 | °CRK |
|  | Gradient limitation offset versus coolant temperature for ignition angle in trailing throttle. |
| IP_IGA_LGRD_PU(_AT)__N_32__MAF_MMV | 4 x 4 | 01...7FFFH | 0,0146...48 | 48 / 32767 | °CRK |
|  | Basic gradient limitation versus engine operating point for ignition angle in trailing throttle. |
| IP_IGA_MAX_PUC__N | 4 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Target ignition angle in case of fast deceleration in trailing throttle (LV_PU). |
| IP_IGA_PUC(_AT)__N | 4 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Target ignition angle in case of trailing throttle fuel cut-off (LV_PUC). |
| IP_IGA_ACCIN_PUC(_AT)__N | 4 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Target ignition angle in case of trailing throttle fuel cut-off (LV_PUC) with air condition compressor active.. |
| C_N_MIN_DHP | 1 | 0...FFH | 0...8160 | 32 | rpm |
| Minimum engine speed to wait for the end of the dashpot function from idle speed control to go to fuel cut-off (LV_PUC). |

Tuning correction ( IGA_AS_(CYL( )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_AS_[CYL] | - | 80...7FH | -48...47,625 | 0,375 | °CRK |
| Tuning correction for individual ignition angle. |

FUNCTION DESCRIPTION:

General information:

The application tool can perform a cylinder individual ignition angle correction using IGA_AS_(CYL( for development (e.g. knock control...).

Application recurrence : 1 sec.

Formula section:

If		IGA_AS_(CYL(  not modified by serial communication line

then	IGA_AS_(CYL( = C_IGA_AS_(CYL(

else		IGA_AS_(CYL( controlled by serial interface until system reset.

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| C_IGA_AS_[CYL] | 1 | 80...7FH | -48...47,625 | 0,375 | °CRK |
| Application system intervention for ignition angle. |

Calculation of basic ignition angle

Basic ignition angle at start ( IGA_ST )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_ST | - | 0...FFH | -23,625...72 | 0,375 | °CRK |
| Basic ignition angle at start (LV_ST). |

Input data:

| LV_ES | LV_ST | N | TCO_ST |
| --- | --- | --- | --- |

FUNCTION DESCRIPTION:

General information:

The basic ignition angle at start (LV_ST) is depending on engine speed N, N_32 and coolant temperature TCO_ST.

It is applied following first ignition angle at engine stopped (LV_ES).

Application recurrence : Segment

Formula section:

IGA_ST = IP_IGA_ST__N__TCO_ST

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_ST__N__TCO_ST | 5 x 8 | 0...FFH | -23,625...72 | 0,375 | °CRK |
|  | Basic ignition angle at start (LV_ST). |

Basic ignition angle out of start ( IGAB )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGAB | - | 0...FFH | -23,625...72 | 0,375 | °CRK |
| Basic ignition angle out of start. |

Input data:

| LV_IS | N | N_32 | MAF |
| --- | --- | --- | --- |
| TCO |

FUNCTION DESCRIPTION:

General information:

The basic ignition angle is depending on engine operating point (N, MAF) and on engine operating states (idle (LV_IS) or out of idle).

Application recurrence : Segment

Formula section:

If	engine operating state idle (LV_IS) active

then	IGAB = IP_IGAB_IS__N__MAF + IP_IGA_TCO_IS__TCO

else		IGAB = IP_IGAB__N__MAF

Endif.

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGAB__N__MAF | 16 x 12 | 0...FFH | -23,625...72 | 0,375 | °CRK |
|  | Basic ignition angle out of start and out of idle. |
| IP_IGAB_IS__N__MAF | 4 x 4 | 0...FFH | -23,625...72 | 0,375 | °CRK |
|  | Basic ignition angle out of start in idle (LV_IS). |
| IP_IGA_TCO_IS__TCO | 6 | 0...FFH | -48...47,625 | 0,375 | °CRK |
|  | Coolant temperature correction of basic ignition angle out of start in idle (LV_IS). |

Basic ignition angle with gradient limitation ( IGA_BAS_LGRD )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_BAS_LGRD | V | 0...FFH | -23,625...72 | 0,375 | °CRK |
| Basic ignition angle with gradient limitation. |

General information:

A gradient limitation is applied to the basic ignition angle calculation IGA_BAS in order to limit ignition angle variations, following the priorities described here below.

Application recurrence : Segment

Engine operating states without gradient limitation for ignition angle.

Input data:

| LV_ISAPWM_IS_ACT | LV_ST | LV_IGA_AST | LV_PUC |
| --- | --- | --- | --- |
| IGA_BAS |

FUNCTION DESCRIPTION:

Formula section:

If		LV_ISAPWM_IS_ACT = 1 (Active)	(idle speed regulation ISAPWM_IS active)

or	engine operating state start ( LV_ST ) active

or	LV_IGA_AST = 1 (Active)	(ignition intervention due to post start function)

or	trailing throttle fuel cut-off ( LV_PUC ) active

then

IGA_BAS_LGRDn = IGA_BASn

Endif.

Gradient limitation for ignition angle at intercept function ( LV_INF )

Input data:

| LV_INF | LV_N_GRD_INF | IGA_BAS | TCO |
| --- | --- | --- | --- |
| C_IGA_LGRD_1 |

FUNCTION DESCRIPTION:

General information:

In case of an important engine speed gradient below a specific engine speed threshold and in closed throttle position, the general gradient limitation C_IGA_LGRD_1 is applied on specific ignition angle IP_IGAB_INF__TCO at intercept function.

Description:

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGAB_INF__TCO | 4 | 0...FFH | -23,625...72 | 0,375 | °CRK |
|  | Basic ignition angle with intercept function (LV_INF) active. |

Re-start fuel feed ( LV_REAC ) at part load ( LV_PUC ( LV_PL )

Input data:

| LV_PUC | LV_PL | LV_REAC | IGA_BAS |
| --- | --- | --- | --- |
| N_32 | TCO | TPS_GRD | IGA_TRA_KNK |
| C_IGA_LGRD_1 | C_IGA_LGRD_2 | C_IGA_LGRD_3 | LV_TRA_KNK_ACT |

FUNCTION DESCRIPTION:

General information:

In order to obtain a soft engine torque built - up, the ignition angle at part load (LV_PL) is retarded and reached with a gradient limitation, depending on the type of acceleration.

The first triggering ignition angle correction for restart fuel feed at part load takes into account the instationary correction (IGA_TRA_KNK).

Description:

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| ID_IGA_RPL__N_32__TCO | 4 x 6 | 0...80H | -48...0 | 0,375 | °CRK |
|  | Ignition angle correction in case of restart fuel feed at part load - First triggering. |
| ID_IGA_LGRD_RPL__N_32 | 4 | 01...7FFFH | 0,00146...48 | 48 / 32767 | °CRK |
|  | Ignition angle gradient limitation for restart fuel feed at part load ( x Segment ). |
| C_TPS_GRD_BOL_RPL | 1 | 0...FFH | 0...2988 | 2988 / 256 | °TPS/sec |
| TPS_GRD threshold for strong or smooth acceleration detection in case of restart fuel feed at part load. |

Re-start fuel feed ( LV_REAC ) at idle ( LV_PUC ( ( LV_PU )( LV_IS )

Input data:

| LV_PUC | LV_PU | LV_IS | LV_REAC |
| --- | --- | --- | --- |
| IGA_BAS | N_32 | N_GRD | LV_PL |
| C_IGA_LGRD_1 | C_IGA_LGRD_2 | C_IGA_LGRD_3 | LV_TRA_KNK_ACT |
| IGA_TRA_KNK | TPS_GRD | ID_IGA_TPS_GRD_TRA__N_32 |

FUNCTION DESCRIPTION:

General information:

In order to obtain a soft engine torque built - down, the ignition angle at idle (LV_IS) is retried and reached with a gradient limitation, depending on the type of deceleration.

Description:

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_LGRD_RIS__N_GRD | 4 | 01...7FFFH | 0,00146...48 | 48 / 32767 | °CRK |
|  | Ignition angle gradient limitation for restart fuel feed at idle (LV_IS) or trailing throttle (LV_PU) ( x Segment ). |

Gradient limitation for ignition angle with anti-jerk correction ( LV_AJ_ACT )

Input data:

| LV_AJ_ACT | IGA_BAS | N_32 | IGA_AJ |
| --- | --- | --- | --- |

FUNCTION DESCRIPTION:

General information:

In order to obtain a soft engine torque built - up following anti-jerk intervention ( IGA_AJ ), the nominal ignition angle is reached with a gradient limitation versus engine speed.

Description:

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| ID_IGA_LGRD_END_AJ__N_32 | 8 | 01...FFH | 0,375...95,625 | 0,375 | °CRK |
|  | Gradient limitation to cancel the anti-jerk ignition angle correction (x Segment). |

Gradient limitation for ignition angle with instationary correction (LV_TRA_KNK_ACT)

Input data:

| LV_TRA_KNK_ACT | IGA_BAS | IGA_TRA_KNK | C_IGA_LGRD_2 |
| --- | --- | --- | --- |

FUNCTION DESCRIPTION:

General information:

In order to obtain a soft engine torque built - up following instationary correction (IGA_TRA_KNK), the nominal ignition angle is reached with the general gradient limitation C_IGA_LGRD_2.

Description:

Gradient limitation for ignition angle with knock detected

Input data:

| KNK_INT_CYL_[CYL] | IGA_BAS |
| --- | --- |

FUNCTION DESCRIPTION:

Formula section:

If		KNK_INT_CYL_(CYL] ( 0

and		IGA_BASn ( IGA_BASn-1

then	IGA_BAS_LGRDn = IGA_BASn

Endif.

Gradient limitation for transition Part Load (PL) -> Idle Speed (IS)

Input data:

| LV_PL | LV_IS |  |
| --- | --- | --- |

FUNCTION DESCRIPTION:

In case of transition Part Load PL -> Idle Speed IS, a specific change limitation C_IGA_LGRD_PL_IS is applied to IGA_BAS_LGRD.

If 	Transition PL -> IS

Then

a change limitation C_IGA_LGRD_PL_IS is applied on IGA_BAS_LGRD until target is 	reached

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| C_IGA_LGRD_PL_IS | 1 | 01...7FFFH | 0,00146...48 | 48 / 32767 | °CRK |
| Ignition angle gradient limitation in case of transition PL->IS |

General gradient limitation for ignition angle

Input data:

| MAF | N | IGA_BAS |
| --- | --- | --- |

FUNCTION DESCRIPTION:

General information:

In specific conditions different from the previous described conditions, a general gradient limitation C_IGA_LGRD_x is applied to the nominal ignition angle in order to limit ignition angle variations.

It´s applied only in advance direction and is different for 3 engine operating areas (MAF, N).

Formula section:

If		MAF ( C_IGA_MAF_LGRD

then	C_IGA_LGRD_x = C_IGA_LGRD_3

else

If	N ( C_IGA_N_LGRD

then	C_IGA_LGRD_x = C_IGA_LGRD_2

else	C_IGA_LGRD_x = C_IGA_LGRD_1

Description:

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| C_IGA_LGRD_1 | 1 | 01...7FFFH | 0,00146...48 | 48 / 32767 | °CRK |
| Ignition angle gradient limitation for area 1 - (x Segment). |
| C_IGA_LGRD_2 | 1 | 01...FFH | 0,375...95,625 | 0,375 | °CRK |
| Ignition angle gradient limitation for area 2 - (x Segment). |
| C_IGA_LGRD_3 | 1 | 01...FFH | 0,375...95,625 | 0,375 | °CRK |
| Ignition angle gradient limitation for area 3 - (x Segment). |
| C_IGA_N_LGRD | 1 | 01...1FE0H | 1...8160 | 1 | rpm |
| Engine speed threshold for ignition angle gradient limitation choice. |
| C_IGA_MAF_LGRD | 1 | 01...FFH | 5,45...1389 | 5,45 | mg/TDC |
| Mass air flow threshold for ignition angle gradient limitation choice. |

Knock control

General - Knock correction ( IGA_KNK_(CYL( )

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IGA_KNK_[CYL] | V | 0...80H | -48...0 | 0.375 | °CRK |
| Cylinder individual ignition angle knock correction. |
| IGA_MV_KNK | V | 0...80H | -48...0 | 0.375 | °CRK |
| Ignition angle knock correction mean value. |

Input data:

| LV_KNK_ACT | LV_KNK_1_ERR | LV_KNK_2_ERR | LV_CAM_ERR_LIH |
| --- | --- | --- | --- |
| LV_TRA_KNK_ACT | LV_IGA_ADJ_TQR | C_IGA_LGRD_3 | LV_CRK_ERR_LIH |
| LV_IGA_CH | LV_TPS_FL | IGA_CH |

Conditions for knock control in normal operation or in limp home

Formula section:

If		LV_KNK_ACT = 1 (Active)		(knock control active)

then

If		LV_KNK_i_ERR = 0		(no error currently present on knock 								 acquisition (sensor n°i) )

and	LV_CAM_ERR_LIH = 0	(no limp home for camshaft sensor)

and	LV_CRK_ERR_LIH = 0	(no limp home for crankshaft 									 sensor)

then		Normal Operation for Knock Control

else		Limp Home Operation for Knock Control

Ignition angle correction out of knock detection area

Formula section:

If		LV_KNK_ACT = 0 (Passive)		(knock control passive)

then

IGA_KNK_(CYL(n = IGA_KNK_(CYL(n-1 + C_IGA_LGRD_3

until		IGA_KNK_(CYL( = 0.

Ignition angle knock correction mean value ( IGA_MV_KNK )

General information:

Application recurrence : 720 °CRK.

Formula section:

NC_CYL_NO

IGA_MV_KNK  =  1 / NC_CYL_NO *	(  IGA_KNK_(CYL									        		CYL = 1

Relative knock corrections limitation

General information:

Application recurrence : 720 °CRK.

Formula section:

If		IGA_KNK_(CYL(  >  ( IGA_MV_KNK + C_IGA_DIF_MAX_MIN_KNK )

then	IGA_KNK_(CYL(  = ( IGA_MV_KNK + C_IGA_DIF_MAX_MIN_KNK )

If		IGA_KNK_(CYL(  <  ( IGA_MV_KNK - C_IGA_DIF_MAX_MIN_KNK)

then	IGA_KNK_(CYL(  = ( IGA_MV_KNK - C_IGA_DIF_MAX_MIN_KNK )

Absolute knock corrections limitation

General information:

To prevent the ignition angle from a too large correction in the retard sense, the knock correction is limited to a maximum value. This maximum value is performed also for diagnosis functions.

Application recurrence : 720 °CRK.

Formula section:

Limit MAXI = IP_IGA_MAX_KNK__N_32__MAF * IP_IGA_TCO_FAC_KNK__TCO

with

Limit MAXI ( 0

and

IGA_KNK_(CYL(  (  Limit MAXI

If			LV_IGA_CH = 1 (Active)

(catalyst heating function active - ignition angle intervention)

and		LV_TPS_FL = 0 (Passive)

(no full load throttle position detected)

then		Limit MAXI = Limit MAXI - IGA_CH

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| IP_IGA_MAX_KNK__N_32__MAF | 8 x 4 | 0...80H | -48...0 | 0.375 | °CRK |
| Maximum ignition angle knock correction versus engine operating point. |
| IP_IGA_TCO_FAC_KNK__TCO | 8 | 00...FFH | 0...0.997 | 3.895E-3 | - |
| Weighting factor versus coolant temperature for determination of maximum ignition angle knock correction. |
| C_IGA_DIF_MAX_MIN_KNK | 1 | 0...80H | 0...48 | 0.375 | °CRK |
| Maximum difference between the individual knock corrections and the ignition angle knock correction mean value. |
| NC_CYL_NO | 1 | 0...FFH | 0...255 | 1 | - |
| Number of Cylinders - Non adjustable calibration. |

Applicative Value :

NC_CYL_NO = 06H = 6 cylinders

Knock control in normal operation

Input data:

| IGA_KNK_[CYL] | N_KNK | LV_IGA_ADJ_TQR | NL_THD_KNK_[CYL] |
| --- | --- | --- | --- |
| MAF_KNK | LV_TRA_KNK_ACT | KNK_INT_CYL_[CYL] |
|  | LV_KNK_ACT | KNKS_[CYL] | ID_IGA_AD_[CYL]__N_KNK__MAF_KNK |

Formula section:

1 - Knock ignition angle correction calculation according to knock ignition angle adaptation.

If		LV_KNK_ACT = 0 (Passive) ( 1 (Active)	( knock control begins active )

then

IGA_KNK_(CYL( = ID_IGA_AD_(CYL(__N_KNK__MAF_KNK

2 - Knock ignition angle correction calculation in case of knock detected :

If		LV_KNK_ACT = 1 (Active)			( knock control continuously active )

then

If	new operating point is detected by the system (N_KNK, MAF_KNK)

then

If	ID_IGA_AD_(CYL(__N_KNK__MAF_KNK

< ( IGA_KNK_(CYL( - C_IGA_AD_DIF_MAX)

then

IGA_KNK_(CYL(n = ( IGA_KNK_(CYL(n-1 - C_IGA_AD_DIF_MAX)

else

If	ID_IGA_AD_(CYL(__N_KNK__MAF_KNK

> ( IGA_KNK_(CYL( + C_IGA_AD_DIF_MAX)

then

IGA_KNK_(CYL(n = ( IGA_KNK_(CYL(n-1+ C_IGA_AD_DIF_MAX)

else

IGA_KNK_(CYL(n = ID_IGA_AD_(CYL(__N_KNK__MAF_KNK

(noise level threshold calculation for knock detection)

If		KNKS_(CYL  (  NL_THD_KNK_(CYL(

then

If	KNK_INT_CYL_(CYL( = 1 (Intensity 1)								( knock is detected with intensity 1 )

then

IGA_KNK_(CYL(n = IGA_KNK_(CYL(n-1 - ID_IGA_DEC_1_KNK__N_KNK

else	    ( ( KNK_INT_CYL_(CYL( = 2 (Intensity 2) : 
					knock is detected with intensity 2 )

IGA_KNK_(CYL(n = IGA_KNK_(CYL(n-1 - ID_IGA_DEC_2_KNK__N_KNK

else			( ( KNK_INT_CYL_(CYL( = 0 (No) : no knock detected )

If		       LV_TRA_KNK_ACT = 0 (Passive)

(no ignition instationary correction requested )

then

IGA_KNK_(CYL(n = IGA_KNK_(CYL(n-1 + ID_IGA_INC_KNK__N_KNK

else

IGA_KNK_(CYL(n = IGA_KNK_(CYL(n-1

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| ID_IGA_DEC_1_KNK__N_KNK | 3 | 01...7FH | 0.375...47.625 | 0.375 | °CRK |
| Update of knock ignition angle correction when knock intensity 1 is detected ( x 720 °CRK ). |
| ID_IGA_DEC_2_KNK__N_KNK | 3 | 01...7FH | 0.375...47.625 | 0.375 | °CRK |
| Update of knock ignition angle correction when knock intensity 2 is detected ( x 720 °CRK ). |
| ID_IGA_INC_KNK__N_KNK | 16 | 01...7FFFH | 0.00146...48 | 0.00146 | °CRK |
| Update of knock ignition angle correction when no knock is detected ( x 720 °CRK ). |
| C_IGA_AD_DIF_MAX | 1 | 0...7FH | 0...47.625 | 0.375 | °CRK |
| Maximum value for updating the knock ignition angle correction. |

Knock control in limp home

General information:

For explanations, refer to the chapter “ Knock Sensors Diagnosis ( KNKS1, KNKS2 ) “ in the major chapter “Diagnosis Management “.

Knock adaptation

Output data:

| Name | Mode | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| LV_IGA_AD_ACT | V | 0...01H | 0...1 | 1 | - |
| Boolean information for knock adaptation loop 1 - ( Passive / Active ). |
| LV_CYC_WUP_KNK | V | 0...01H | 0...1 | 1 | - |
| Boolean information for warm up cycle fulfilled |

Input data:

| LV_KNK_ACT | LV_KNK_1_ERR | LV_KNK_2_ERR | LV_IS |
| --- | --- | --- | --- |
| LV_N_GRD_MAX_KNK | LV_TPS_GRD_TRA_KNK | LV_TPS_ERR | LV_MAF_ERR |
| LV_TCO_ERR | LV_TIA_ERR | LV_ISA_1_ERR | LV_ISA_2_ERR |
| LV_LSH_UP_1_ERR | LV_LSH_UP_2_ERR | LV_CAM_ERR | LV_CRK_ERR |
| LV_IGA_ADJ_TQR | LV_STATE_A_MIS | LV_STATE_B_MIS | MAF_KNK |
| LV_IGA_CH | LV_TPS_FL | LV_SCC_TQR | N_32 |
| LV_VLS_LIM_1_ERR | LV_VLS_LIM_2_ERR | IGA_MV_KNK | N_KNK |

General information:

The adaptation assists the knock ignition angle correction IGA_KNK_(CYL( during transition from an engine operating point to another one.

An indexed table ID_IGA_AD_(CYL( __N_KNK__MAF_KNK is provided for each cylinder.

They are updated with the value of IGA_KNK_(CYL( determined for each operating point by the knock control.

Formula section:

If		LV_KNK_ACT = 1 (Active)

(knock control active)

and	LV_KNK_i_ERR = 0

(no error currently present on knock sensors)

and	LV_IS = 0

(engine operating state out of idle)

and	LV_N_GRD_MAX_KNK = 0 (Passive)

(no engine speed dynamics relative to knock control)

and	LV_TPS_GRD_TRA_KNK = 0 (Active)

(no load dynamics relative to knock control)

and	LV_TPS_ERR = 0

(no error currently present on throttle position sensor)

and	LV_MAF_ERR = 0

(no error currently present on mass air flow sensor)

and	LV_TCO_ERR = 0

(no error currently present on coolant temperature sensor)

and	LV_TIA_ERR = 0

(no error currently present on air temperature sensor)

and	LV_ISA_i_ERR = 0

(no error currently present on idle charge actuator command signal (coil i))

and	LV_LSH_UP_i_ERR = 0

(no error currently present on oxygen sensor upstream heater power stage)

and	LV_CAM_ERR = 0

(no error currently present on camshaft sensor)

and	LV_CRK_ERR = 0

(no error currently present on crankshaft sensor)

and	LV_DUR_IGC_(CYL(_ERR = 0

(no error currently present on the corresponding ignition output)

and	LV_IV_(CYL(_ERR = 0

(no error currently present on corresponding injector power stage)

and	LV_STATE_A_MIS = 0

(no misfire status CARB A (catalyst damage))

and	LV_STATE_B_MIS = 0

(no misfire status CARB B (increase emissions))

and		MAF_KNK ( ID_MAF_MIN_AD_KNK__N_32

and		LV_IGA_CH = 0 (Passive)

(no catalyst heating function with ignition angle intervention)

or	LV_TPS_FL = 1 (Passive)

(full load throttle position detected)

then

LV_IGA_AD_ACT = 1 (Active)

(knock adaptation loop 1 authorized)

and

ID_IGA_AD_(CYL(__N_KNK__MAF_KNK = IGA_KNK_(CYL]

else

LV_IGA_AD_ACT = 0 (Passive)

Remark :

- Storing the adaptation values ( ID_IGA_AD_(CYL( ) from knock adaptation loop in non volatile memory with ECU in power-latch :

The adaptation values from the indexed tables ID_IGA_AD_(CYL( are initialized  to 0 if one of the following conditions are fullfilled:

-Virginal ECU

-Request from service tester

-EEPROM read failure

Each time during power latch: it is the mean value IGA_MV_KNK which is stored for each operating point. Thus, the 6 adaptation indexed tables ID_IGA_AD_(CYL( are equal.

All indexed tables ID_IGA_AD_(CYL( are increased by C_IGA_INC_AD degrees up to the maximum 0 if:

- LV_CYC_WUP_KNK = 1

- TCO was above 71°C at the last engine stop (vehicle was driven until engine warm)

- TCO has increased by more than 21°C since last engine stop

Thus, it is possible to slowly reduce high values once learnt, without the necessity to

approach these points in steady state.

LV_CYC_WUP_KNK:

Conditions to reset: 	System reset

Conditions to set:	If 	LV_CYC_WUP = 1

then 	LV_CYC_WUP_KNK = 1

Calibration data:

| Name | Dim | Hex. limits | Phys. limits | Resol. | Unit |
| --- | --- | --- | --- | --- | --- |
| ID_MAF_MIN_AD_KNK__N_32 | 16 | 0...FFH | 0...1389 | 5.45 | mg/TDC |
| Minimum engine load to take into account knock adaptation. |
| ID_IGA_AD_[CYL]__N_KNK__MAF_KNK | 16 x 4 | 0...80H | -48...0 | 0.375 | °CRK |
| Cylinder individual ignition angle knock adaptation. |
| C_IGA_INC_AD | 1 | 0...10H | 0...6 | 0.375 | °CRK |
| Offset on ignition angle knock adaptation value when engine stopped. |